DIGITAL DESIGN COEN 312 Instructor: Asim J. Al-Khalili

Time Allowed 3:00 hrs. All questions carry equal marks Final Summer, 2010 No materials are allowed 2 Pages

Question 1

- Design a network that adds either 1 or 2 to a 3-bit binary number N (n2, n1, n0). The network output is M (m3, m2, m1, m0).  K is a control signal.

When K = 0, M = N + 1

K =1,  M = N + 2

b)  Implement m3 using a 4-to-1 multiplexer with minimum external logic.

Fig 1 Adder to be designed of Question 1

Question 2

Design a 4-bit binary number to 7 segment decoder. The decoder should show if the number is a multiple of 2 or 3 as shown ( use 2 when the number can be divided by 2 and 3) . Please refer to Fig. 2 below for the segment’s destination. Assume that all other numbers will be displayed as E.

Give circuit Implementation.

Fig. 2. 7-Segment Display of Question 2

## Question 3

Using K-Map minimize the following function F

- F (A,B,C,D) = m(0,2,5,7,12,14) + d (8,10, 13, 15) Give results in SOP form.

- Implement in NAND-NAND from

- Implement in NOR_NOR form

- Implement in AND_OR_NOT from

Question 4

- Represent the following by a Boolean equation.

The outdoor light “L” should be turned on if there is nobody at home ”N” , the time is between 8 p.m. and 5 a.m “T”. and it is not a holiday “H”.

- Using Boolean Algebra, show that the two functions f1 and f2 are equal:

f1(a,b,c) = a’c + b’c’ + ab

f2(a,b,c) = a’b’ + bc + ac’

- Using Boolean Algebra, minimize the following function:

f(a,b,c,d) = ac’ + ab’d + a’b’c + a’cd’ + b’c’d’

- Give the maxterm list equivalent of the following function:

f(a,b,c) = ab

## Question 5

Design a clocked sequential circuit with 4 outputs. The outputs are to drive colored lights:  Red, R, Yellow, Y, Blue, B and Green, G consecutively and repeatedly in the same order ie: R→Y→B→G→R → Y→………… Start the design with the state diagram and follow standard design procedure. What is the frequency of operation if each light is to stay ON for 1 second. Neglect all logic and FlipFlop delays.

Question 6

Analyze the circuit given below fully. Determine Excitation equations, Transition table and the State diagram. Explain what function the circuit performs.

Solution:

Q1

#1 a)

|  | h | n2 | n1 | n0 | m3 | m2 | m1 | m0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |
| 2 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 |
| 3 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 |
| 4 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 |
| 5 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |
| 6 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 |
| 7 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 |
| 8 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 9 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 |
| 10 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 |
| 11 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 |
| 12 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 |
| 13 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 |
| 14 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 |
| 15 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |

| h n2 n1 n0 |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 |  |  |  |  |
|  | 01 |  |  |  |  |
|  | 11 |  | 1 | 1 |  |
|  | 10 |  |  | 1 |  |

m3=∑m(7,14,15)

m3=n2n1n0 + hn2n1

| h n2 n1 n0 |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 |  | 1 | 1 |  |
|  | 01 |  | 1 | 1 |  |
|  | 11 | 1 |  |  | 1 |
|  | 10 |  | 1 |  | 1 |

m2=∑m(3,4,5,6,10,11,12,13)

m2=n2n1’ + hn2’n1 + n2’n1n0 + h’n2n1’

| h n2 n1 n0 |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 |  |  | 1 | 1 |
|  | 01 | 1 | 1 | 1 | 1 |
|  | 11 |  |  |  |  |
|  | 10 | 1 | 1 |  |  |

m1=∑m(1,2,5,6,8,9,12,13)

m1=hn1’ + n1’n0 + h’n1n0’

| h n2 n1 n0 |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 | 1 | 1 |  |  |
|  | 01 |  |  | 1 | 1 |
|  | 11 |  |  | 1 | 1 |
|  | 10 | 1 | 1 |  |  |

m0= ∑m(0,2,4,6,9,11,13,15)

m0= hn0 + h’n0’

m3= n2n1n0 + hn2n1

m2=n2n1’ + hn2’n1 + n2’n1n0 + h’n2n1’

m1=hn1’ + n1’n0 + h’n1n0’

m0= (h⊕n0)’

Assuming double rail

b)

m3= n2n1n0 + hn2n1= n2n1(n0 + h)

OR

m3= h’n2n1n0 + hn2n1n0 + hn2n1n0’ = n2n1(h’n0 + hn0 + hn0’)

Q2

|  | A3 | A2 | A1 | A0 | 7 Segment | a | b | c | d | e | f | g |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | E | 1 | 0 | 0 | 1 | 1 | 1 | 1 |
| 1 | 0 | 0 | 0 | 1 | E | 1 | 0 | 0 | 1 | 1 | 1 | 1 |
| 2 | 0 | 0 | 1 | 0 | 2 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |
| 3 | 0 | 0 | 1 | 1 | 3 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |
| 4 | 0 | 1 | 0 | 0 | 2 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |
| 5 | 0 | 1 | 0 | 1 | E | 1 | 0 | 0 | 1 | 1 | 1 | 1 |
| 6 | 0 | 1 | 1 | 0 | 2 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |
| 7 | 0 | 1 | 1 | 1 | E | 1 | 0 | 0 | 1 | 1 | 1 | 1 |
| 8 | 1 | 0 | 0 | 0 | 2 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |
| 9 | 1 | 0 | 0 | 1 | 3 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |
| 10 | 1 | 0 | 1 | 0 | 2 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |
| 11 | 1 | 0 | 1 | 1 | E | 1 | 0 | 0 | 1 | 1 | 1 | 1 |
| 12 | 1 | 1 | 0 | 0 | 2 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |
| 13 | 1 | 1 | 0 | 1 | E | 1 | 0 | 0 | 1 | 1 | 1 | 1 |
| 14 | 1 | 1 | 1 | 0 | 2 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |
| 15 | 1 | 1 | 1 | 1 | 3 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |

a=d=g= “1” and b=f’ and c=e’

| A3 A2 A1 A0 |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 |  | 1 | 1 | 1 |
|  | 01 |  |  | 1 |  |
|  | 11 | 1 |  |  | 1 |
|  | 10 | 1 | 1 | 1 | 1 |

b=A2’A1+A0’A2+A0’A3+A3A2A1’

| A3 A2 A1 A0 |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 |  |  |  |  |
|  | 01 |  |  |  | 1 |
|  | 11 | 1 |  | 1 |  |
|  | 10 |  |  |  |  |

c=A3’A2’A1A0+A3A2’A1’A0+A3A2A1A0

a=d=g=∑m(0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,15)

b=∑m(2,3,4,6,8,9,10,12,14,15)

c=∑m(3,9,15)

e=∑m(0,1,2,4,5,6,7,8,10,11,12,13,14)

f=∑m(0,1,5,7,11,13)

Q3

a)

| A B C D |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 | 1 |  | 1 | X |
|  | 01 |  | 1 | X |  |
|  | 11 |  | 1 | X |  |
|  | 10 | 1 |  | 1 | X |

F=BD + AD’+B’D’

b) F= (BD + AD’+B’D’)” = ((BD )’(AD’)’(B’D’)’)’

Assuming double rail

c)

| A B C D |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 |  | 0 |  | X |
|  | 01 | 0 |  | X | 0 |
|  | 11 | 0 |  | X | 0 |
|  | 10 |  | 0 |  | X |

F=(B+D’)(A+B’+D)

d)

| A B C D |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
|  | 00 |  | 1 |  | X |
|  | 01 | 1 |  | X | 1 |
|  | 11 | 1 |  | X | 1 |
|  | 10 |  | 1 |  | X |

F’=B’D+A’BD’

Q4

- L=> output

N=> someone is home

T=> Time is between 8 PM & 5 AM

H=> is a holiday

L= N’+H’

- Many ways of doing this problem. This is the simplest:

a’c+b’c’+ab=a’b’+bc+ac’ expand both sides

a’c(b+b’)+b’c’(a+a’)+ab(c+c’)=a’b’(c+c’)+bc(a+a’)+ac’(b+b’)

a’bc+a’b’c+ab’c’+a’b’c’+abc+abc’= a’bc+a’b’c+ab’c’+a’b’c’+abc+abc’

∑m(0,1,3,5,6,7) = ∑m(0,1,3,5,6,7)

- ac’+ab’d+a’b’c+a’cd’+b’c’d’

ab’d+a’b’c=ab’d+a’b’c+b’cd		(eg ab+a’c+bc=ab+a’c)

ac’+ab’d+a’b’c+b’cd+a’cd’+b’c’d’

ac’+ab’d+a’cd=ac’+b’cd

ac’+b’cd+a’b’c+a’cd’+b’c’d’

b’cd+a’b’c+a’cd’=b’cd+a’cd’

f=ac’+b’cd+a’cd’+b’c’d’

| ab c |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 00 | 01 | 11 | 10 |
| 0 |  |  | 1 |  |
| 1 | 1 |  | 1 |  |

F=∏M(0,1,2,3,4,5)

Q5

|  | present | next | R | Y | B | G |
| --- | --- | --- | --- | --- | --- | --- |
| 00 | A | B | 1 | 0 | 0 | 0 |
| 01 | B | C | 0 | 1 | 0 | 0 |
| 10 | C | D | 0 | 0 | 1 | 0 |
| 11 | D | A | 0 | 0 | 0 | 1 |

| Y1 Y0 | 0 | 1 |
| --- | --- | --- |
|  | 0 |  | 1 |
|  | 1 | 1 |  |

Y1+=Y1⊕Y0

| Y1 Y0 | 0 | 1 |
| --- | --- | --- |
|  | 0 | 1 | 1 |
|  | 1 |  |  |

Y0+=Y0’

| present | next | output |
| --- | --- | --- |
| Y1 | Y0 | Y1 | Y0 | R | Y | B | G |
| 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |
| 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 |

B=01  C=10  D=11

Using D-FF

Y+=D

Y1+=Y1⊕Y0

Y0+=Y0’

Frequency of operation: 1sec * 4 = 4sec=.25 Hz

Q6

Y+=D

Y2+=X

Y1+=Y2	Excitation Equations

Y0+=Y1

Z=Y0

|  |  |  |  |  | X=0 | X=1 | output |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Transition Table |  | Y2 | Y1 | Y0 | Y2+ | Y1+ | Y0+ | Y2+ | Y1+ | Y0+ | Z |
|  | A | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
|  | B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
|  | C | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 |
|  | D | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |
|  | E | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 |
|  | F | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 |
|  | G | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 |
|  | H | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 |

|  |  | Next | output |
| --- | --- | --- | --- |
|  | present | X=0 | X=1 | z |
| State Table | A | A | E | 0 |
|  | B | A | E | 1 |
|  | C | B | F | 0 |
|  | D | B | F | 1 |
|  | E | C | G | 0 |
|  | F | C | G | 1 |
|  | G | D | H | 0 |
|  | H | D | H | 1 |

The function of this circuit is a 3-bit right shift register.

State Diagram:

# Text boxes

e

b

a

Adder to be designed

g

a

d

b

c

g

a

N

M

K

g

d

d

f

e