Course Number Section Modern/Integrated Circuit Filter Design ELEC 441 WW

Examination Date Time # of pages Mid-Term Test#2 April 2, 2012 70 minutes 3

Instructor(s) Dr. R. Raut

Only ENCS approved calculator allowed Crib-sheet with hand-written formula on two sides of a A-sized paper allowed.

Special Instructions: (Read very carefully) Attempt ALL questions Show all steps clearly in neat and legible handwriting. Students are required to return question paper together with exam booklet(s).

Q.1: The intermediate frequency filter in a GSM cellular phone system has the transfer function

Provide the design of one of the second order sections above using OTA and C elements. The capacitors must be below 10pF in value. Calculate the gm  and C values in your design.

Q.2: (a) Perform pre-warping on the zero and the pole frequencies in the transfer function  , and derive the associated Switched Capacitor Filter (SCF) transfer function H(z), using bilinear s (> z transformation. Use a sampling frequency of 16 kHz.

(b) What will be the response of the SCF at (a) DC, and (b) 492 rad/sec?

The attached Table may be used for your calculations

Table (related to Q.2)

Q.3:

Figure 3

Figure 3 shows a  second order switched capacitor filter using parasitic insensitive switched capacitor integrators. 1, 2 are non- overlapping clock signals of period T.  Find an expression for the Z-domain  transfer function . You can assume that the sample-and-hold property holds for the signals  Vi , and V1 i.e.,  etc.,.

Q.4: The schematic in Figure 4 represents a normalized low-pass Bessel-Thomson filter of order 3 with equal terminating resistances.

Figure 4

Use frequency dependent negative resistance (FDNR) technique, and show a design of the filter with terminations, and a pass-band edge frequency of 3000 radians.

Show your schematic and the designed element values clearly.